AstrAlim Specification
Revision 0.1-47
DGE
Wednesday, November 22, 2023

AstrAlim
This page intentionally blank
Table of Contents

 Revision History
Revision	Date	Contributor	Comments
0.1-09	12/11/2023	D.Germa	Initial Revision
0.1-23	13/11/2023	D.Germa	Work on power supply and other sections.

# Introduction

## Document Management
This Libre Office document resides at the following URL: https://hsanchezii.wordpress.com

This document’s status is: Work-in-progress.
## Acronyms
GPIO	General Purpose Input/Output
USB	Universal Serial Bus
NafaBox	Nomad Astronomie For All

## General context :
The purpose of NafaBox-Hardware, which was born at the end of 2018, is to be able to offer to everyone plug-in electronic cards for a Raspberry Pi (or a card with a compatible 40-pin connector) dedicated to amateur astronomers.

The NafaBox-Hardware is designed in order to offer the capacity to drive a complete set of telescope hardware with minimal cabling, and in the context of Nomadism, where the power supply is a 12V batterie.

The NafaBox is there to provide for a device concentrator. Limiting cabling for the telescope devices.
The NafaBox provides for a CPU enabling to leave the telescope operating alone during the night with minimal power consumption.
The NafaBox provides for power management.

Device to take into account :
1. Mount (12V alimentation, EQMOD (USB) Interface.
2. Main cooled camera (12V alimenation, USB3 interface)
3. Guide Camera (USB3 interface)
4. Heat strips for drew management.
5. Focuser step motor.
6. Temperature sensors. (E.g. DS18B20)
7. Humidity pressure and temperature sensor (E.g.: I2c BME280 or DHT22)
8. GPS sensor for easy positioning and time management.
9. RTC clock.

The NafaBox-Hardware is meant to be used with Indi interface library.
The NafaBox-Hardware is meant to be used with a Raspberry pi computer which provides for the Software interface to the user PC.

Target software to be run on the NafaBox set are : kstars, VNC, specifics, …

The NafaBox is currently made of a rapsberry PI4 with 4 stacked hats.

## User requirements :
With regards to the NafaBox original the requirements are :
The Astralim board is designed to offer as many functions as the original 4 board while maintaining software compatibility.
If possible, it aims to leverage the stacking principle to introduce additional functions in the future while preserving the initial stacking concept.

### Context of usage :
The solution shall provide the electronic and power distribution to enable astrophtogaphie.
The solution shall be usable in mobility, but as well as fixed installation.
The solution shall be usable remotely.

### Computation capacity and user interface :
The solution shall provide the computational power needed to prepare and run autonomously the night of Astrophotography.
The solution shall enable the user to take of it’s laptop from the telescope setup while the telescope is continuing operations.
### Time and positioning :
The solution shall include a saved clock in order for the computer for correct skymap working.
The solution sall include a GPS for correct earth positioning.
The solution shall include a GPS for a precise time synchronization (lower than ms). This will enable occultation measurements (Step below special Camera setup).
### Licencing :
The solution shall enable opensource software solutions.
### Power management and mobility :
In moblity, the power needed is a battery. As a consequence the solution shall be usable with a quite standard power solution. (12V battery pack).

In mobility we shall be able to monitor power consumption of the different elements.
We shall be able to cut the power of unneeded elements.
In particular during mission preparation, only a small set of element shall be powered on.

When power from the electrical grid is available, it shall be possible to supply 12V through an external switched-mode power supply. (Compatibility aspect)
### Setup to be managed :
The setup includes :
1. A main cooled astronomic camera (USB3 and 12V cooling standard interfaces).
2. A guiding camera.
3. Anti drew hater.
# List of requirements
## Context and hypothesis :
### Needs for 5V power and constraints :
#### Power consumptions of equipments connected to raspberry :
- RPI4 USB output :
  - All of the models with 4 USB ports have a maximum USB port output of 1.2A for all 4 ports combined, with no per-port limits (meaning, all 1.2A is available on a single port if no others are in use).
- RPI5 USB Output :
  - When using a standard 5V, 3A (15W) USB-C power adapter with Raspberry Pi 5, by default we must limit downstream USB current to 600mA to ensure that we have sufficient margin to support these workloads. This is lower than the 1.2A limit on Raspberry Pi 4
- USB 3 : 900 mA
- Camera : Mainly USB3 type B with no specific characteristics => 900mA. (Wikipedia)
  - Main Camera :
    - ASI533-MC : Camera Power consumption: 650mA at 5V
  - Guide: idem ASI553.
- EQMod interface : Negligibl.
- Memory :
  - PI5 Case : Nvme 1To power consumption : 1A
#### Power consumptions of equipments connected to raspberry :
- RPI5 : RPI : Stress test : 12W (5V 2,4A )
- RPI4 : 400% CPU load (stress --cpu 4) 1280 mA (6.4 W)
##### Total :
- RPI4 : Min 5V, 3A.
  - (650mA * 2 Camera) maximisé par 1,2A pour la some des USB + 1280 mA (stress test) = 2480mA
  - Soit 12,4W
  - On a surestimé les camera
- RPI5 : Min 5V, 4.7A.
  - (650mA * 2 Camera) + 1A pour Nvme + Stress 2,4A
  - Total : 4700mA
  - Soit 23,5W
### Needs for 12V power and constraints :
#### Mount power consumption :
Example of mount power consumption :
- EQ8 : 12V 4.6A
- HEQ6 : 12V 2A
- ZWO AM3 : 12V 1.7A
- ZWO AM5 : 12V 1.5A
- CQ350 : 12V 3A
Capacity to cut power enable to provide for a remote reset of the mount in case of bug of the goto part of the mount.
#### Camera Cooler :
- ARES-C Pro : 12V 2,5A
- ASI533-MC : 12V at 3A Max
- ASI2400MC : Cooling : 12V@3A DC
#### Heat Strip:
12V 0.2W /cm = 12V 0,02A
60mm guide scope => 0,7A
200mm Main mirror : 2,4A

#### Total:
Taking out EQ8 which is not movable : 12V 9A.
#### Using RPI GPIO for power input unlocking limitation :
Official documentation : Powering Raspberry Pi 5
PI4 :Physical/Board pin 2
RPI EEPROM : Github

Need to add to bootconfig.txt : “usb_max_current_enable=1”
## General Requirements :
# REQ1 : The board shall take power from a 12V DC source.
# REQ2 : The board shall be protected by a resettable fuse 10A
# REQ3 : The board shall be protected against polarity inversion of the power source.
# REQ5 : The board shall contain a Raspberry hat 40pin gpio connector.
# REQ6 : The board shall connect the ground to all GPIO ground pins.
## Price Targets :
REQ18 : The price of the board shall not be greater than 150€.
## Raspberry compatibility :
# REQ9 : The board shall be compatible with Raspberry PI4.
# REQ11 : The board shall be compatible with Raspberry PI5.
#### 5V Outputs:
Rational for the following requirements : See analysis section 3.1.1..
# REQ10 : The board shall provide the capacity to provide the 5V to the raspberry.

# REQ10.1 : Hyp 1 : via all the GPIO pins controlled by a dipswitch.
Rational : the PI5 raspberry limits the current to 500mA to it’s USB outputs, and may provide for limited operations if the power is not provided by the USB-C connector.
# REQ10.2 : Hyp 2 : via all the USB-C raspberry connector.
Rational : In this hypothesis an external connector is needed (E.g. : LinkAdaptor).
# REQ10.3 : Hyp 3 : The power is provided through the GPIO, with 5A capacity.
The /boot/config.txt contains usb_max_current_enable=1 as expressed in section 3.1.2.5. should enable appropriate USB power output for the cameras.
# REQ7 : The board shall include a DC-DC step down circuit that will provide 5V 5A (25W) power from 12V input power. (see REQ10.1, REQ10.2 and REQ10.3)
E.g.: DC-DC TRACOPOWER, THL 25
## 12V Outputs :
Need :
- Termal regulation of camera.
- 2 heat strips for Guide, primary, and secondary
- Power for mount.
# REQ12 : A measurement of out power shall be provided for each output.
# REQ13 :The board shall provide a controllable 12V 3A outputs for external device interfacing. (Mount)
# REQ21 : The board shall provide a controllable 12V 3A outputs for external device interfacing. (Cooler)
# REQ14 : The board shall provide two PWM-controllable 12V 3A outputs for interfacing with heater strips.

## 9V Outputs :
# REQ8 :The board shall include a DC-DC step down circuit that will provide 9V 3A power.
## Focuser :
Rational for the following requirements : The indi driver astroberry-diy driver for kstars provides for an appropriate interface..
# REQ15 : Provide either DRV8834 and A4988 stepper controllers.
# REQ16 : Interface STEP, DIR, MS1, MS2, MS3 shall be connected to the GPIO.
# REQ24 : The Focuser component shall be inserted as a removable component too enable change of the component in case of bad usage of the driven motor.
## GPS :

Pps signal ?
# REQ25GPS : A module GPS shall be included with a SMA connector to enable external antenna.
E.g.: NEO-6M (Amazon) or NEO-6M (AliExpress)

## Physical format and stacking constraints :
# REQ4 : The board format shall be a Raspberry Hat format.
# REQ17 : The board high shall be a multiple of 11mm high for GPIO connector compatibility. (To be reworded).
## Drew environmental sensors :
# REQ22 : Temperature sensor that can be external to the board enclosure.
E.g.: 1wire connector for DS18B20
# REQ23 : humidity, pressure and temperature sensor.
E.g.: BME280.
## Thermal aspect :
# TBD

## Compatibility with other NAFABox boards :
# REQ19 : The Atralim shall be compatible with other NafaBox Hardware if the functionality is not completely replaced.
# REQ20 : The Astralim shall be compatible with other NafaBox hardware if addition of the original Nafa Board does add functionality to the complete set.
# Implementation strategie
## Connectors:
### 12V
### USB
### 9V
### GPS
### Focuser
## Price management:
The following table gives a price evaluation:

REQ		Prix TTC €
REQ7	DC-DC TRACOPOWER, THL 25	72,46

## Requirement compliance (Traceability and rational) :
Requirement Number	Rational for implementation or rejection	Implemented (Yes/no)

## Compatibility with other NafaBox board folowup.
In the view of the preliminary conception the Astralim provides for all functions of the NafaRes, and NafaAlim board.
=> compatibility is not needed save for the Software aspect.

Pin	Fct			NAFA Base	NAFA Relay	AstrAlim	Astralim Changes
1	3.3V
2	5V
3	GPIO 2	I2C SDA		RTC		PowerSensor1,2,3,4 Pwm Out 3, Pwm Out 4
4	5V
5	GPIO 3	I2C SCL		RTC		PowerSensor1,2,3,4 / Pwm Out 3, Pwm Out 4
6	GND
7	GPIO 4					1 Wire
8	UART TX					Gps
9	GND
10	UART RX					Gps
11	GPIO 17				Relay1	Relay1
12	GPIO 18		PWM0		Relay2	Relay2
13	GPIO 27				Focus Dir
14	GND
15	GPIO 22				Relay3	GPS PPS
16	GPIO 23				Relay4
17	3.3V
18	GPIO 24				Focus RST	Focuser DIR
19	GPIO 10	SPI0 MOSI
20	GND
21	GPIO 9	SPI0 MISO					GPS PPS
22	GPIO 25				Focus Step	Focuser Step
23	GPIO 11	SPI0 SCLK
24	GPIO 8	SPI0 CS0
25	GND
26	GPIO 7	SPI0 CS1
27	0
28	GPIO 1
29	GPIO 5
30	GND
31	GPIO 6						Relay1
32	GPIO 12		PWM0	FAN		Focuser MS2
33	GPIO 13		PWM1				Relay2
34	GND
35	GPIO 19	SPI1 MISO	PWM1				Focuser MS1
36	GPIO 16	SPI1 CS0				Focuser MS1	Focuser MS2
37	GPIO 26						Focuser Slp
38	0	SPI1 MOSI					Focuser Step
39	GND
40	GPIO 21	SPI1 SCLK					Focuser DIR

I2C Adress		A0	A1	A2	Function	Component	Board
0x69[1]	0110 1001[2]				RTC	DS3231MZ	NafaBase

0x41	0100 0001	3.3V	Gnd		Measure Out 1	INA219AIDR	Astralim
0x44	0100 0100	Gnd	3.3V		Measure Out 2	INA219AIDR	Astralim
0x49	0100 1001	3.3V	SDA		Measure Out 3	INA219AIDR	Astralim
0x4D	0100 1101	3.3V	SCL		Measure Out 4	INA219AIDR	Astralim
0x50	0101 0000	Gnd	Gnd	Gnd	Pwm Out 3 [3] / (Set duty / Shut Down /recall)	DS1050Z-005	Astralim
0x51	0101 0001	Gnd	Gnd	Gnd	Pwm Out 4 / (Read pwm duty)	DS1050Z-005	Astralim
0x54	0101 0100	Gnd	3.3V	Gnd	Pwm Out 3 [4] / (Set duty / Shut Down /recall)	DS1050Z-005	Astralim
0x55	0101 0101	Gnd	3.3V	Gnd	Pwm Out 4 / (Read pwm duty)	DS1050Z-005	Astralim
[1] May be set at first time setup.
[2] May be set at first time setup.
[3] In shutdown mode output will be high impedance. With regards to the Astralim design which has a pull own resistor, this mode will shut off the output consistently.
[4] In shutdown mode output will be high impedance. With regards to the Astralim design which has a pull own resistor, this mode will shut off the output consistently.

# Another Major Heading
## Example Figure
These instructions work for LibreOffice version 7.1.2.2
To add a figure do:
1. Insert→ Image
2. Right Click on Figure, Anchor → As Character
3. Right Click on Figure, Wrap → None
4. Right Click on Figure, Insert Caption
5. Optional. If you want to add fancy borders around the figure, Right Click on figure, Properties → Borders; Adjust to taste
To add a Table of Figures move the cursor to an appropriate part of the document. Preferably, at the top of a forced new page start. Then do the following:
1. Insert Table of Contents and Index → Table of Contents, Index, or Bibliography
2. Title: Fill in to taste
3. Select: Table of Figures

Figure 1: Sample Code Monster
# Appendices