AstrAlim Specification
Revision 0.1-18
DGE
Monday, November 13, 2023

AstrAlim
This page intentionally blank
Table of Contents

 Revision History
Revision	Date	Contributor	Comments
0.1-09	12/11/2023	D.Germa	Initial Revision
0.1-16	13/11/2023	D.Germa	Work on power supply and other sections.

# Introduction

## Document Management
This Libre Office document resides at the following URL: https://hsanchezii.wordpress.com

This document’s status is: Work-in-progress.
## Acronyms
GPIO	General Purpose Input/Output
USB	Universal Serial Bus

# List of requirements
## Context and hypothesis :
### Needs for 5V power and constraints :
#### Power consumptions of equipments connected to raspberry :
- RPI4 USB output :
  - All of the models with 4 USB ports have a maximum USB port output of 1.2A for all 4 ports combined, with no per-port limits (meaning, all 1.2A is available on a single port if no others are in use).
- RPI5 USB Output :
  - When using a standard 5V, 3A (15W) USB-C power adapter with Raspberry Pi 5, by default we must limit downstream USB current to 600mA to ensure that we have sufficient margin to support these workloads. This is lower than the 1.2A limit on Raspberry Pi 4
- USB 3 : 900 mA
- Camera :
  - Main:
    - ARES-C Pro :
      - Camera maximum power consumption: ≈ 30w
      - Camera maximum working current: ≈2.5A
      - USB: Work on PI4
      - Proposed Cooling power suply : 12V 5A
    - ASI533-MC
      - Camera Power consumption: 650mA at 5V
      - Cooler Power consumption: 12V at 3A Max
    - ASI2400MC :
      - Cooling : 12V@3A DC
  - Guide:
    - idem ASI553.
- EQMod interface :
- Memory :
  - PI5 Case : Nvme 1To power consumption : 1A
#### Power consumptions of equipments connected to raspberry :
- RPI5 : RPI : Stress test : 12W (5V 2,4A )
- RPI4 : 400% CPU load (stress --cpu 4) 1280 mA (6.4 W)
##### Total :
- RPI4 : Min 5V, 2,98A.
- RPI5 : Min 5V, 3.7A.
#### Using RPI GPIO for power input unlocking limitation :
Official documentation : Powering Raspberry Pi 5
PI4 :Physical/Board pin 2
RPI EEPROM : Github

Need to add to bootconfig.txt :

usb_max_current_enable=1
## General Requirements :
# REQ1 : The board shall take power from a 12V DC source.
# REQ2 : The board shall be protected by a resettable fuse xxA
# REQ3 : The board shall be protected against polarity inversion of the power source.
# REQ5 : The board shall contain a Raspberry hat 40pin gpio connector.
# REQ6 : The board shall connect the ground to all GPIO ground pins.
#
## Price Targets :
REQ18 : The price of the board shall not be greater than 150€.
## Raspberry compatibility :
# REQ9 : The board shall be compatible with Raspberry PI4.
# REQ11 : The board shall be compatible with Raspberry PI5.
#### 5V Outputs:
Rational for the following requirements : See analysis section 2.1.1..
# REQ10 : The board shall provide the capacity to provide the 5V to the raspberry.
# REQ10.1 : Hyp 1 : via all the GPIO pins controlled by a dipswitch.
Rational : the PI5 raspberry limits the current to 500mA to it’s USB outputs, and may provide for limited operations if the power is not provided by the USB-C connector.
# REQ10.2 : Hyp 2 : via all the USB-C raspberry connector.
Rational : In this hypothesis an external connector is needed (E.g. : LinkAdaptor).
# REQ10.3 : Hyp 3 : The power is provided through the GPIO, with 5A capacity.
The /boot/config.txt contains usb_max_current_enable=1 as expressed in section 2.1.1.3. should enable appropriate USB power output for the cameras.
# REQ7 : The board shall include a DC-DC step down circuit that will provide 5V 5A power from 12V input power. (see REQ10.1 and REQ10.2)
## 12V Outputs :
Need :
- Termal regulation of camera.
- 2 heat strips for Guide, primary, and secondary
- Power for mount.
# REQ12 : A measurement of out power shall be provided for each output.
# REQ13 :The board shall provide two controllable 12V outputs for external device interfacing.
# REQ14 : The board shall provide two PWM-controllable 12V outputs for interfacing with external devices.

## 9V Outputs :
# REQ8 :The board shall include a DC-DC step down circuit that will provide 9V 3A power.
## Focuser :
Rational for the following requirements : The indi driver astroberry-diy driver for kstars provides for an appropriate interface..
# REQ15 : Provide either DRV8834 and A4988 stepper controllers.
# REQ16 : Interface STEP, DIR, MS1, MS2, MS3 shall be connected to the GPIO.
## GPS :
Pps signal ?

## Physical format and stacking constraints :
# REQ4 : The board format shall be a Raspberry Hat format.
# REQ17 : The board high shall be a multiple of 11mm high for GPIO connector compatibility. (To be reworded).
## Thermal aspect :
# TBD

## Compatibility with other NAFABox boards :
# TBD
# Implementation strategie
## Connectors:
### 12V
### USB
### 9V
### GPS
### Focuser
## Price management:
## Requirement compliance (Traceability and rational) :
Requirement Number	Rational for implementation or rejection	Implemented (Yes/no)

# Another Major Heading
## Example Figure
These instructions work for LibreOffice version 7.1.2.2
To add a figure do:
1. Insert→ Image
2. Right Click on Figure, Anchor → As Character
3. Right Click on Figure, Wrap → None
4. Right Click on Figure, Insert Caption
5. Optional. If you want to add fancy borders around the figure, Right Click on figure, Properties → Borders; Adjust to taste
To add a Table of Figures move the cursor to an appropriate part of the document. Preferably, at the top of a forced new page start. Then do the following:
1. Insert Table of Contents and Index → Table of Contents, Index, or Bibliography
2. Title: Fill in to taste
3. Select: Table of Figures

Figure 1: Sample Code Monster
# Appendices